How to Update BIOS by AwardBIOS flash Utility

on FWA-3240 ?

NOTE: The following instructions is based on AwardBIOS Flash Utility V8.59G and using FWA-3240 as an example, different versions of Award BIOS Flash Utility may act differently. Please make sure that the tool you have in hand is working with the BIOS file or not…

- Create a DOS boot up disk, USB or floppy disk.

- Copy BIOS file and Awdflash utility to disk

- Power on the system & boot up by disk.

- Type in the Awardflash executable file name and the BIOS file name.

EX : C:\> awd859g 3240v180.bin

- Choose to save or not save original BIOS file?

No necessary to save original BIOS file if you have back up on hand…

- When the BIOS is successfully updated, the following screen will be displayed.

Note : If you see the following message:

"The program file's part number does not match with your system."

Please make sure that you have the correct BIOS file and use the following command:

(Awdflash program name) (BIOS file name)

ex: awd859g 3240v180.bin

Wade Peng

Application Engineer

Network Computing Group, Advantech Corp.