How to Update BIOS Using Awdflash

NOTE: The following instructions is based on awd854b and using AIMB-742 and PCA-6187 as an example, different versions of Awdflash may act differently. Please make sure that the awdflash you have in hand is working with the BIOS file you have.

- Create a DOS boot up disk.

- Copy BIOS file and Awdflash to a floppy disk.

- Start the system which requires BIOS update and boot up with the floppy disk created.

- Type in the Awdflash executable file name and the BIOS file name as shown on the picture.

- Choose to save or not save original BIOS file or not.

- When the BIOS is successfully updated, the following screen will be displayed.

If you see the following message:

"The program file's part number does not match with your system."

Please make sure that you have the correct BIOS file and use the following command:

(Awdflash program name) (BIOS file name) /f

ex: awd854b 6187e204.bin /f